## Slide 1: Topics
Basic knowledge review
Hand “CNI” with Linux tools

## Slide 2: 0. Prerequisites
Network protocol stack(MAC/ARP/IP/ICMP/TCP/UDP)
Bridging/Switching(VLAN/VxLAN) and Routing(subnet/netmask, gateway/nexthop, route lookup)
Linux commands(ip, iptables, conntrack, …)
Container/Linux namespaces(Network, Mount, UTS, IPC, User)
Kubernetes installation and operation
Notes: Wolf 秦柯 TCP IP
CCNA/JNCIA
马哥教育

## Slide 3: 1. Linux host(Network protocol stack) is a Multi-Function Router/Switch/Firewall
NICs
Network Namespace(ip netns)
tun/tap(virtual NIC)
bridge(ip, bridge(iproute2)/brctl(bridge-utils))
veth pair
iptables
Notes: Enable IPv4 forwarding:
# echo 1 > /proc/sys/net/ipv4/ip_forward
How to confirm which 2 veth interfaces are a pair:
ethtool –S eth0
ip link show eth0
cat /sys/class/net/eth0/iflink; cat /sys/class/net/vethxxxx/ifindex

## Slide 4
NIC
NIC
Linux Host
Linux Kernel
tun
OpenVPN
Application 1
Application 2
Application N
Pod F
Pod H
Pod C
Linux Bridge
VM 1
VM 2
VM N
tap
Network Protocol Stack
Socket API Layer
Linux Bridge
Pod V
Notes: Tap: Layer 2 virtual NIC
Tun: Layer 3 virtual NIC
Veth pair: veth1@veth2, veth2@veth1
Linux bridge: slave ports can be tap, veth, NIC

## Slide 5
worker2
worker1
worker3
vnet#6/host-only
192.168.210.0/24
enp0s9
192.168.210.22/24
enp0s9
192.168.230.23/24
Leaf03
vnet#7/host-only
192.168.230.0/24
Laptop
enp0s9
192.168.210.21/24
swp1/vlan210
192.168.210.254/24
mgmt/eth0
192.168.100.103/24
vnet/host-only
192.168.100.0/24
enp0s8
192.168.100.21/24
enp0s8
192.168.100.22/24
enp0s8
192.168.100.23/24
swp2/vlan230
192.168.230.254/24

## Slide 6: Hand CNI - 1 Containers connected under Linux bridge on the same node
Diagram(container-to-container)
Network Stack
netns1
192.168.10.1/24
netns3
192.168.10.3/24
eth0
eth0
veth1
veth3
worker1.k8s.com
br0

## Slide 7: Hand CNI - 2 Containers connected to host network stack on the same node
Diagram(container-to-container)
Network Stack
netns1
192.168.10.1/32
netns3
192.168.10.3/32
eth0
eth0
veth1
veth3
worker1.k8s.com
192.168.10.254/32
Notes: How to avoid wasting IP addresses in such scenario:
Use /31 for each netns, which will waste one IP address for each netns
Use /32 for each netns, which makes the veth pair as a point-to-point link, and we can use the same IP for all veth belongs to the host Network Stack.(We also use an IP of other physical interface as well, or a link local IP address, or enable proxy_arp for veth and don’t assign any IP)
https://askubuntu.com/questions/893097/how-to-get-rid-of-169-254-0-0-route
# vi /etc/network/if-up.d/avahi-autoipd
….
if [ -x /bin/ip ]; then
# route already present?
ip route show | grep -q '^169.254.0.0/16[[:space:]]' && exit 0
/bin/ip route add 169.254.0.0/16 dev $IFACE metric 1000 scope link
elif [ -x /sbin/route ]; then
# route already present?
/sbin/route -n | egrep -q "^169.254.0.0[[:space:]]" && exit 0
/sbin/route add -net 169.254.0.0 netmask 255.255.0.0 dev $IFACE metric 1000
fi

## Slide 8: Break 1

## Slide 9
https://n0where.net/how-does-it-work-iptables

## Slide 10: Hand CNI - 3 Container connected under Linux bridge go to outside
Diagram(container-to-outside)
br0
192.168.10.254/24
netns1
192.168.10.1/24
eth0
veth1
enp0s9
192.168.210.21/24
swp1: 192.168.210.254/24
Leaf03
worker1.k8s.com

## Slide 11
NIC
Linux Host
Linux Kernel
Pod 1
Network Protocol Stack - Netfilter
Socket API Layer
Linux Bridge
PREROUTING - raw
Connection Tracking
PREROUTING - mangle
For this host?
FORWARD - filter
POSTROUTING - Snat
FORWARD - mangle
PREROUTING - nat
POSTROUTING - mangle
N
Notes: Iptables –vnL –t nat
conntrack -L

## Slide 12: Hand CNI - 4 Client container access ClusterIP whose backend container is on the same node
Diagram(container-to-ClusterIP_service)
br0
192.168.10.254/24
Client netns1
192.168.10.1/24
Server netns3
192.168.10.3/24
eth0
eth0
veth1
veth3
worker1.k8s.com
ClusterIP
11.96.10.3:8080
HTTP service
192.168.10.200:80

## Slide 13
NIC
Linux Host
Linux Kernel
Service Pod
Network Protocol Stack - Netfilter
PREROUTING - raw
Connection Tracking
PREROUTING - mangle
For this host?
FORWARD - filter
POSTROUTING - nat
FORWARD - mangle
PREROUTING - Dnat
POSTROUTING - mangle
Client Pod
Linux Bridge
N
Notes: Iptables –vnL –t nat
conntrack -L

## Slide 14: Hand CNI - 5 Outside or Client container access NodePort whose backend container is on the same node
Diagram(outside-to-NodePort_service)
br0
192.168.10.254/24
enp0s9
192.168.210.21/24
Leaf03
worker1.k8s.com
NodePort
192.168.210.21:32080
Server netns3
192.168.10.3/24
eth0
veth3
HTTP service
192.168.10.3:80
swp1: 192.168.210.254/24

## Slide 15
NIC
Linux Host
Linux Kernel
Application
Service Pod
Network Protocol Stack - Netfilter
PREROUTING - raw
Connection Tracking
PREROUTING - mangle
For this host?
FORWARD - filter
POSTROUTING - nat
FORWARD - mangle
PREROUTING - Dnat
POSTROUTING - mangle
Linux Bridge
N
Routing
Decision
OUTPUT - raw
Connection Tracking
OUTPUT - mangle
OUTPUT - Dnat
Routing
Decision
OUTPUT - filter
Notes: Iptables –vnL –t nat
conntrack -L

## Slide 16: Break 2

## Slide 17: Hand CNI - 6 Containers connected under Linux bridges on different nodes - IPIP
Diagram(container-to-container)
br0
192.168.10.254/24
netns1
192.168.10.1/24
eth0
veth1
enp0s9
192.168.210.21/24
tunl0
192.168.10.2/32
worker1.k8s.com
br0
192.168.30.254/24
netns1
192.168.30.1/24
eth0
veth1
enp0s9
192.168.230.23/24
tunl0
192.168.30.2/32
worker3.k8s.com
worker2.k8s.com
enp0s9
192.168.210.22/24
br0
192.168.20.254/24
tunl0
192.168.20.2/32
Route | NextHop
192.168.210.0/24 | swp1
192.168.230.0/24 | swp2
swp1
192.168.210.254/24
swp2
192.168.230.254/24
Notes: https://developers.redhat.com/blog/2019/05/17/an-introduction-to-linux-virtual-interfaces-tunnels#ipip_tunnel
When the ipip module is loaded, or an IPIP device is created for the first time, the Linux kernel will create a tunl0 default device in each namespace, with attributes local=any and remote=any.
When receiving IPIP protocol packets, the kernel will forward them to tunl0 as a fallback device if it can't find another device whose local/remote attributes match their source or destination address more closely.

## Slide 18: Hand CNI - 7 Containers connected under Linux bridges on different nodes - VxLAN
Diagram(container-to-container)
br0
192.168.10.254/24
netns1
192.168.10.1/24
eth0
veth1
enp0s9
192.168.210.21/24
vxlan100
192.168.10.4/32
00:00:ff:ff:10:04
worker1.k8s.com
br0
192.168.30.254/24
netns1
192.168.30.1/24
eth0
veth1
enp0s9
192.168.230.23/24
vxlan100
192.168.30.4/32
00:00:ff:ff:30:04
worker3.k8s.com
worker2.k8s.com
enp0s9
192.168.210.22/24
br0
192.168.20.254/24
vxlan100
192.168.20.4/32
00:00:ff:ff:20:04
Route | NextHop
192.168.210.0/24 | swp1
192.168.230.0/24 | swp2
swp1
192.168.210.254/24
swp2
192.168.230.254/24
Notes: https://developers.redhat.com/blog/2019/05/17/an-introduction-to-linux-virtual-interfaces-tunnels#ipip_tunnel
When the ipip module is loaded, or an IPIP device is created for the first time, the Linux kernel will create a tunl0 default device in each namespace, with attributes local=any and remote=any.
When receiving IPIP protocol packets, the kernel will forward them to tunl0 as a fallback device if it can't find another device whose local/remote attributes match their source or destination address more closely.

## Slide 19: OpenVPN application
Diagram of OpenVPN client and site
OpenVPN ping
Network Stack
tun0: 10.18.130.65
Internet
VPN Site
Office
Network
10.23.130.195
10.23.130.1
a.b.c.d

## Slide 20: OpenVPN application
Check ip address and ip route before connecting VPN to a site
Check ip address and ip route after connecting VPN to a site

## Slide 21: Break 3

## Slide 22: Hand CNI - 8 Containers connected under Linux bridges on different nodes – Static route
Diagram(container-to-container)
br0
192.168.10.254/24
netns1
192.168.10.1/24
eth0
veth1
enp0s9
192.168.210.21/24
worker1.k8s.com
br0
192.168.30.254/24
netns1
192.168.30.1/24
eth0
swp1
192.168.210.254/24
enp0s9
192.168.230.23/24
swp2
192.168.230.254/24
worker3.k8s.com
worker2.k8s.com
enp0s9
192.168.210.22/24
br0
192.168.20.254/24
Route | NextHop
192.168.210.0/24 | swp1
192.168.230.0/24 | swp2
192.168.10.0/24 | 192.168.210.21
192.168.20.0/24 | 192.168.210.22
192.168.30.0/24 | 192.168.230.23
veth1

## Slide 23: Hand CNI - 9 Containers connected under Linux bridges on different nodes – BGP
Diagram(container-to-container)
br0
192.168.10.254/24
netns1
192.168.10.1/24
eth0
veth1
enp0s9
192.168.210.21/24
worker1.k8s.com
br0
192.168.30.254/24
netns1
192.168.30.1/24
eth0
veth1
enp0s9
192.168.230.23/24
worker3.k8s.com
worker2.k8s.com
enp0s9
192.168.210.22/24
br0
192.168.20.254/24
swp1
192.168.210.254/24
swp2
192.168.230.254/24
Route | NextHop
192.168.210.0/24 | swp1
192.168.230.0/24 | swp2
192.168.10.0/24 | 192.168.210.21
192.168.20.0/24 | 192.168.210.22
192.168.30.0/24 | 192.168.230.23
Notes: # apt install bird
# cat /etc/bird/bird.conf
# This is a minimal configuration file, which allows the bird daemon to start
# but will not cause anything else to happen.
#
# Please refer to the documentation in the bird-doc package or BIRD User's
# Guide on http://bird.network.cz/ for more information on configuring BIRD and
# adding routing protocols.
# Change this into your BIRD router ID. It's a world-wide unique identification
# of your router, usually one of router's IPv4 addresses.
router id 192.168.210.22;
# The Kernel protocol is not a real routing protocol. Instead of communicating
# with other routers in the network, it performs synchronization of BIRD's
# routing tables with the OS kernel.
protocol kernel {
scan time 60;
import all;
export all; # Actually insert routes into the kernel routing table
}
# The Device protocol is not a real routing protocol. It doesn't generate any
# routes and it only serves as a module for getting information about network
# interfaces from the kernel.
protocol device {
scan time 60;
}
protocol direct {
interface "br0";
}
protocol bgp upstream {
import all;
export where source = RTS_DEVICE;
local as 65002;
source address 192.168.210.22;
neighbor 192.168.210.254 as 65000;
}

## Slide 24: Kubernetes CNI introduction
https://www.cni.dev/plugins/current/

## Slide 25: What does a CNI do?
IPAM(IP address+Subnetmask, routes)
  Node level
  Cluster level
Connect Pod to others
  Pod to Pod on the same node
  Pod to Pod on the different nodes(Tunnel, Routing), mustn’t have NAT
  Pod to Outside
  Pod to Service(ClusterIP)
  Outside to Service(NodePort)

## Slide 26: Break 4